## Slide 1: ABE Labs 1.1 and 1.2 Tools of the Trade

## Slide 2
CHAPTER 1:
Some Tools of the Trade
Lab 1.1
2014

## Slide 3
Purpose of Lab 1.1
Become familiar with the small volumes of solutions used in molecular biology
Introduce proper use of the micropipette
Practice using the micropipette
http://kcts9.pbslearningmedia.org/resource/biot11.sci.life.gen.usingmicro/using-a-micropipette/

## Slide 4
Micropipettes

## Slide 5
Parts of the Micropipette

## Slide 6
Micropipette Use
Twist dial to desired volume
Add disposable pipette tip
Press plunger to first stop
To retrieve liquid, slowly release plunger
To transfer liquid, press plunger past first stop to second stop
Keep plunger down as you remove pipette
Eject tip

## Slide 7
Reading a P-20 Micropipette

## Slide 8
Reading a Micropipette (cont.)
0
5
0
0
5
0
0
5
0
5 μL
50 μL
500 μL
P-20
P-200
P-2000

## Slide 9
Micropipetting “Nevers”
Never use a micropipette without a tip
Never lay a micropipette down with sample in the tip
Never let the plunger button snap back
Never set the micropipette outside its range (for example, a P20 pipette below 2.0μL or above 20.0μL)

## Slide 10
Pipetting Techniques
Hold micropipette and microfuge tubes at eye level when loading or dispensing samples

## Slide 11
Place both elbows on the table and use your other hand to stabilize the bottom of the pipette
Pipetting Techniques (cont.)

## Slide 12
Practice Pipetting Sheet
20 μL
0
0
0
0
15 μL
0
0
0
0
10 μL
0
0
0
0
5 μL
0
0
0
0
2 μL
0
0
0
0

## Slide 13
CHAPTER 1:
Some Tools of the Trade
Lab 1.2
2014

## Slide 14
Purpose of Lab 1.2
Become familiar with gel electrophoresis
Practice using the micropipette to load wells in practice plates
Practice running an electrophoresis gel using three dyes: xylene cyanole, bromophenol blue, and orange G

## Slide 15
Magnified Agarose Matrix

## Slide 16
Loading Gels
Insert pipette tip:
Under buffer level
Above gel well
Running an Agarose Gel:
http://kcts9.pbslearningmedia.org/resource/biot11.sci.life.gen.agaroserun/running-an-agarose-gel/

## Slide 17
Improper Loading Technique
Tip is in the well
Tip punched through the gel
Dye spreading under the well

## Slide 18
Analysis of Sample Composition
A
B
C
Sample A has blue and purple dye
Sample B has blue, purple, and yellow dye
Sample C has blue dye

## Slide 19
A
B
C
Heaviest is blue dye (xylene cyanole)
Middle is purple dye (bromophenol blue)
Lightest is yellow dye (orange G)
Predicted Dye Molecular Weights

## Slide 20
Heaviest is purple dye (bromophenol blue) – 670.0 amu
Middle is blue dye (xylene cyanole) – 538.6 amu
Lightest is yellow dye (orange G) – 452.4 amu
Actual Dye Molecular Weights

## Slide 21
Purple dye (bromophenol blue) has more negative charge per unit of mass than blue dye (xylene cyanole) due to presense of bromine ions
The heavier purple dye molecule travels farther through the gel than the lighter blue dye molecule
Dye Molecular Weight Discrepency